## Slide 1
Power relay for EV charaging system
Hongfa Product Solution

## Slide 2: EV Systems
AC/DC
Charging Points
Portable Charger
电磁锁
Electric System
Power System
APS
Charging System
BMS
02

## Slide 3: OBC
IEC61851-1：2017
200VDC-450VDC
CHN：220 VAC或380 VAC
EU：230 VAC或 400 VAC
US：120 VAC或 240 VAC
AC-DC converter consist of
PFC + DC-DC
03
Recommended（-T：105℃）
≤16A：HF115F/K-T，HF152F/D-T
32A： HF178F/-T，HF165F-50（105℃）
＞60A: HF176F,HF186F（105℃）
Requirements
IEC61851-1，GB/T18487.1
50000 cycles, before rectification
230A 100μs inrush
Long time carrying
ambient temperature 85℃~105℃

## Slide 4: OBC
❶
❶
❹
❷
❷
❸
❸
❸
❹
❹
❶
Single phase input
HF186F：55A @105℃
HF161F-40W：40A @105℃
HF189F：48A @85℃ with auxiliary contact
❷
3 phase input
HF161F-40W：40A @105℃
HF179F-W：32A @105℃
HF190F：32A @85℃ with auxiliary contact
❸
Pre-charge
HF179F-W：32A @105℃
❹
Lines switching
HF179F-W：16/32/16A 600VAC @105℃
HF190F：32A @85℃ with auxiliary contact
Multifunction-V2X
Single/3 phase charging
Vehicle to Grid
Vehicle to Vehicle
Vehicle to Load
04
Recommended:

## Slide 5: Portable Charger for Mode 2
IEC 62752:5.3.2
I≤32A
Single Phase
U~120/230VAC
Three Phase
U~240/400/480 VAC
Function Box
In-Cable Control and Protective Device for Mode2
Control pilot function
Residual current function
Switching device
Requirement（IEC62752, GB/T18487.1, NB/T42077）
Short-circuit current with SCPD
Overvoltage category 2, U>230V: 2.5kV，1.5mm gap
Recommended：
≤16A: HF115FK, HF152F,
＞16A: HF178F, HF161F-W/40W, HF165F, HF179F/-W*, HF190F*, HF189F*, HF170F, HF177F*, HF185F
(Products marked with * can be withstand up to 1.5kA short-circuit current according to IEC62752 without welding, for more detail, please contact Hongfa team.)
NB/T 42077:5.3.2
I≤16A
Single Phase
U~230VAC
05

## Slide 6: AC/DC Charging Station for Mode 3/4
DC Station, Mode 4 IEC61851-23
Power Module（AC-DC）
HF165FD(30A)
HF165FD-50(32/40/50A)
RDC-DD
IEC 62955
Breaker/Disconnector
500A or 10 times rated current on/off 3 times
6000A short-circuit current
AC
DC
DC/AC
AC Station, Mode 3 IEC61851-1/ GB/T 18487.3
A： Single Phase
220V 16A
B： Single/Three Phase
220/380V 32A
7.2kW ~3-4h (22kw for three phase)
C： Three Phase
U≤660V， 32A≤I≤250A
Requirements
Overvoltage category 3, 4kV, gap ≥3mm
Monitor the switching contacts
SCPD
Products
HF179F/-W(32A, 1.8/2.4mm)
HF165F(43A, 1.8/2.0mm)
HF176F(65A, 3mm)
HF186F(66A, 3mm)
*#HF177F(954)(A46)(40A,2.3mm)
#HF170F/2H(40A,3.6mm)
*#HF187F/4H(40A,3.9mm)
#HF189F(48A,2.25mm)
#HF190F(32A,2.25mm)
# aux. contact is optional
Requirements of DC output relay
HVDC
Auxiliary contact
06

## Slide 7: Products in EV System
电磁锁
APS
OBC AC Side （-T：105℃）
≤16A：HF115F/K-T(882)，HF152F/D-T(882)
32A： HF178F/-T，HF165F-50
>60A : HF176F, HF186F
Magnetic Lock of Charging Gun
HFD2,HFD3,HF32FV
IC-CPD
HF115F/K-T(16A,105℃）
HF179F/-W(32A 105℃，1.8/2.4mm)
HF161F-W(33A, 1.5/1.8mm)
HF161F-40W（40A 105℃，43A 85℃，2mm）
HF190F(32A 2.25mm with auxiliary contact)
HF189F(48A 2.25mm with auxiliary contact)
Grid input
AC to DC
like OBC AC side
Insulation Monitor
HF181F
HFD3-VI
AC Station output
HF177F/2H(954)(A46)(40A,2.3mm)
HF187F/4H1D(32A,3.9mm)
HF179F/-W(32A,1.8/2.4mm)
HF165F(43A, 2mm)
HF170F(40A, 3.6mm)
HF170F/2H1D with aux. contact
HF186F(66A, 3mm)
......
APS control
HF115F
HF92F
HF116F
HF30F
Fan Motor
HF32FV
HF33F
HF46F
Car window, wipe etc. in Electric System
Auto Relays
DC output/Quick Charge input
HVDC
Main Relay
HVDC
BMS
OBC DC Side
HVDC
Precharge Relay
HVDC
Battery Monitor
Signal Relay
AC/DC
Charging
Stations
07

## Slide 8: Product Map for AC charger
16A
32A
65A
HF115F/FK
HF165F-50
HF161F-W
STD:33A,1.5mm
477:33A, 1.8mm
456:33A, 2.0mm
704:26A, 2.3mm
A27:35A,2.3mm
HF165FD(30A)
HF178F 1A&1C
40A
HF165F-50
STD:40A 85℃
50A 65℃
60A 60℃
A21: 60A @85℃
HF176F, 3mm
STD:65A
A37:80A
HF152F/D
85℃
105℃
HF152F/D-T
HF115F/FK-T
HF178F-T
HF179F, 1.8mm
HF179F-W, 2.4mm
Ambient temp.
Current
HF170F/2A(3.6mm)
HF170F/2A+1B
with auxiliary contact
HF161F-40W, 2mm
STD:43A
A21:50A
HF189F, 2.25mm
48A with auxiliary contact
HF190F, 2.25mm
32A with auxiliary contact
HF187F/4A+1B,3.9mm
40A with auxiliary contact
HF185/2A, 3.0mm
50A 277VAC 85℃
HF177F(954)/2A,2.3mm
40A/35A
HF198F/2A,3.6mm【developing】
40A with auxiliary contact
HF186, 3.0mm
55A 105℃
66A 85℃
HF165F, 43A
STD:1.8mm,43A
797:2.0mm,43A
A21:2.0mm,60A

## Slide 9: Featured products
Contact rating：
HF115F 8A/12/16A 250VAC 85℃
HF115F-H 10A 250VAC 85℃
HF115F-Q 16A 250VAC 125℃
HF115F-T 16A 250VAC 105℃
Features：
1) Creepage distance: ≥10mm
Dielectric strength（coil-contacts): ≥5000VAC
Meet IEC60335-1
2) Temp. 85℃/105℃（-T）/125℃（-Q）
Productivity:
Automatic production, annual output >100 million pcs.
HF115F/HF115F-H/HF115F-I/
HF115F-Q/HF115F-T
HF152F/HF152F-T
Contact rating:
HF152F 1H: 20A 125VAC/17A 277VAC
1Z: 16A 250VAC
HF152F-T: 105℃
Feathers:
1) Size: 21×16×20.6 mm
2) Coil power: 360mW
Productivity:
Automatic production, annual output >20 million pcs.
09

## Slide 10: Featured products
Contact arrangement: 1 Form A
Contact rating: 26~33A 250VAC 85℃
2HP 250VAC
*35A type is optional
Size: 30.4×15.9×23.3 mm
Contact gap: 1.5/1.8/2.0/2.3mm
Dielectric strength (coil-contacts): ≥ 4500VAC
HF161F-W
10
HF165FD
Contact arrangement: 1 Form A
Contact rating: 40A 250VAC
30A 250VAC
2HP 240VAC
TV-8 125VAC
Size: 32.2×27.5×20.4mm
HF165F
Contact arrangement: 1 Form A
Contact rating: 35/43A 250VAC
*60A type is optional
Size: 32.2×27.4×15.4mm
Contact Gap: ≥1.8/2.0mm
Dielectric strength (coil-contacts): ≥2500VAC

## Slide 11: New products
HF178F/HF178F-T
HF179F/HF179F-W
HF165F-50
Size: 21.5x16x20.6mm(the same as HF152F)
Contact rating:
HF178F/HF178F-T: 85℃/105℃, 32A current-carrying
HF179F/HF179F-W: Gap=1.8/2.4mm,
16A-32A-16A 600VAC 105℃
Withstands up to 1.5kA short circuit current
(according to IEC62752) (Standard type coil)
Approval: UL/TUV/CQC
Mass production
HF161F-40W
Size: 30.4×15.9×23.3 mm(the same as HF161F-W）
Contact rating: 40A @105℃, 43A @85℃
*50A type is optional
Contact gap: 2.0/1.8mm
Approval: UL/TUV/CQC
Mass production
Size: the same as HF165F
Contact rating:
32A 105℃/40A 85℃/50A 65℃/60A 60℃
*60A @85℃ type is optional
Approval: UL/TUV/CQC
Mass production
11

## Slide 12: New products
Size: 36x30x40mm
Contact arrangement: 2 Form A
Contact gap: ≥3.6mm
Contact rating:
40A 277VAC 85℃
Approval: UL/TUV/CQC
Mass production
HF176F
HF186F
Size: 30x20x31mm
Contact gap: ≥3mm
Contact rating:
20A/55A/20A 277VAC 105℃
20A/66A/20A 600VAC 85℃
Approval: UL/TUV/CQC
Mass production
HF170F/2H
HF170F/2H1D
Size: 38x33x36.3mm
Contact gap: ≥3mm
Contact rating:
20A/65A/20A 400VAC 85℃
*80A type is optional
Approval: UL/TUV
Mass production
Contact arrangement:
2 Form A+1 Form B
Approval: UL/TUV/CQC
Mass production
With 1 form B aux. contact
12
Tiny

## Slide 13: New products
Size: 35x25x28mm
Contact arrangement: 1 Form A+1 Form B
Contact gap: ≥2.25mm
Contact rating: 48A 277VAC 85℃(Main contact)
Withstands up to 1.5kA short circuit current
(according to IEC62752)
Approval: UL/TUV
Mass production
HF190F
HF189F
Size: 35x16x28mm
Contact arrangement: 1 Form A+1 form B
Contact gap: ≥2.25mm
Contact rating: 32A 277VAC 85℃ (Main contact)
Withstands up to 1.5kA short circuit current
(according to IEC62752)
Approval: UL/TUV
Mass production
With 1 form B aux. contact
With 1 form B aux. contact
13
HF185F
Size: 40x35x38.8mm
Contact arrangement: 2 Form A
Contact gap: ≥3.0mm
Contact rating: 50A 277VAC 85℃
Approval: UL/TUV
Mass production

## Slide 14: New products
Size: 38x35x47mm
Contact arrangement: 2 form A+1 form B
Contact gap：≥3.6mm
Contact rating：40A 440VAC 85℃
Withstands up to 3kA short circuit current
(according to IEC62955)
MP: Q1/2023
HF198F
HF187F
Size: 59x35x47mm
Contact arrangement: 4 Form A+1 Form B
Contact gap: ≥3.9mm
Contact rating: 40A 277VAC 85℃(Main contact)
Withstands up to 3kA short circuit current
(according to IEC62955)
Approval: UL/TUV/CQC
Mass production
With 1 form B aux. contact
HF177F(954)
Size: 50x25x31mm
Contact arrangement: 2 Form A
Contact gap: ≥2.3mm
Contact rating: 40A/35A 277VAC 85℃
Withstands up to 4.5kA short circuit current
(according to IEC62955)
Approval: UL/TUV/CQC
Mass production
EU AC Charging
14
With 1 form B aux. contact
Developing

## Slide 15: Thanks
Contact us
Website: www.hongfa.com
Tel: 189604550106
E-mail: power-product05@hongfa.com
Power Relay Dept. of HQ Marketing Center
Xiamen Hongfa Electroacoustic Co.,Ltd.
Rev.2 2211